## Slide 1
Introduction to OpenFOAM
Open Source Computational Fluid Dynamics
Microcredential Module 1
Moodle-Compatible Learning Resource
OpenFOAM v13 / v2506

## Slide 2
Introduction to OpenFOAM — Microcredential Module 1
2 / 28
Learning Objectives
By the end of this module, you will be able to:
Explain what OpenFOAM is and its role in Computational Fluid Dynamics (CFD)
Describe the fundamental governing equations solved by OpenFOAM
Identify the key components of the OpenFOAM case directory structure
Outline the three-stage CFD workflow: pre-processing, solving, post-processing
Recognize the major solver categories and their applications
Understand the Finite Volume Method (FVM) as the core numerical technique
Appreciate the open-source ecosystem and community resources

## Slide 3
Introduction to OpenFOAM — Microcredential Module 1
3 / 28
What is Computational Fluid Dynamics?
Definition
CFD is the use of applied mathematics, physics, and computational software to visualize how a gas or liquid flows — and how it affects objects as it flows past them.
Instead of building physical prototypes and running expensive wind tunnel tests, engineers can simulate fluid behavior computationally — saving time and cost.
CFD Predicts
Fluid flow patterns and velocity fields
Pressure distributions on surfaces
Temperature and heat transfer rates
Chemical reactions and combustion
Turbulent mixing and dispersion
Multiphase interactions (gas-liquid)

## Slide 4
Introduction to OpenFOAM — Microcredential Module 1
4 / 28
What is OpenFOAM?
Open Source Field Operation And Manipulation
A free, open-source C++ toolbox for CFD with 1.5+ million lines of code, used by thousands of engineers and researchers worldwide.
Free & Open Source
Licensed under GNU GPL v3. No license fees, ever.
C++ Codebase
1.5M+ lines of high-performance C++ code with OOP design.
Active Community
Thousands of users globally across industry and academia.
Bi-Annual Releases
Regular updates: v2506 (ESI) and v13 (Foundation).

## Slide 5
Introduction to OpenFOAM — Microcredential Module 1
5 / 28
History of OpenFOAM
1993
FOAM created at Imperial College London by Henry Weller
2004
Released as OpenFOAM under GNU GPL by OpenCFD Ltd
2011
OpenFOAM Foundation established; SGI acquires OpenCFD
2014
ESI Group acquires OpenCFD; dual release streams begin
2020
Major growth in industrial adoption and GPU computing
2025-26
OpenFOAM v13 (Foundation) and v2506 (ESI) released

## Slide 6
Introduction to OpenFOAM — Microcredential Module 1
6 / 28
OpenFOAM Variants
Two main distributions maintained by different organizations
openfoam.com (ESI/OpenCFD)
Maintained by OpenCFD Ltd (ESI Group)
Versioning: vYYMM (e.g., v2506)
Bi-annual releases (June & December)
Strong industrial feature focus
Extensive documentation & tutorials
openfoam.org (Foundation)
Maintained by The OpenFOAM Foundation
Integer versioning (e.g., v13)
Led by CFD Direct (Henry Weller)
Emphasis on code quality & design
Modular solver framework

## Slide 7
Introduction to OpenFOAM — Microcredential Module 1
7 / 28
Governing Equations of Fluid Flow

## Slide 8
Introduction to OpenFOAM — Microcredential Module 1
8 / 28
Finite Volume Method (FVM)

## Slide 9
Introduction to OpenFOAM — Microcredential Module 1
9 / 28
Why Finite Volume Method?
Conservative
Flux entering one cell exactly equals flux leaving its neighbor — no artificial mass/energy creation.
Handles Complex Geometry
Works with unstructured meshes: tetrahedra, hexahedra, polyhedra — real engineering shapes.
Physically Intuitive
Each cell is a tiny control volume where conservation laws are enforced — direct physical interpretation.
Robust for CFD
Natural treatment of source terms, boundary conditions, and discontinuities in the flow field.

## Slide 10
Introduction to OpenFOAM — Microcredential Module 1
10 / 28
The CFD Simulation Workflow

## Slide 11
Introduction to OpenFOAM — Microcredential Module 1
11 / 28
Stage 1: Pre-Processing
Geometry Definition
Define the computational domain using CAD tools or OpenFOAM's built-in blockMeshDict. Import external geometries in STL or OBJ format for complex shapes.
Mesh Generation
Create the computational grid using blockMesh (structured), snappyHexMesh (automatic hex-dominant), or external tools like cfMesh and Gmsh.
Boundary Conditions
Specify inlet velocities, outlet pressures, wall types (no-slip, slip), symmetry planes, and periodic boundaries in the 0/ directory.
Physical Properties
Set fluid properties: viscosity, density, turbulence model parameters, and transport properties in the constant/ directory.

## Slide 12
Introduction to OpenFOAM — Microcredential Module 1
12 / 28
Meshing in OpenFOAM
blockMesh
Structured hex mesh generator
Best for simple geometries (pipes, channels, boxes). Defined in system/blockMeshDict with vertices, blocks, and grading.
Advantages:
High quality hex cells
Full control over grading
Fast generation
snappyHexMesh
Automatic hex-dominant mesher
Handles complex CAD surfaces (STL). Automatically refines, snaps to geometry, and adds boundary layers.
Advantages:
Handles complex geometries
Automatic surface refinement
Built-in layer addition

## Slide 13
Introduction to OpenFOAM — Microcredential Module 1
13 / 28
Stage 2: Solving
The solver reads the case setup, assembles the discretized equations, and iterates toward a converged solution.
1
Select the Solver
Choose from 80+ solvers based on your physics: simpleFoam (steady incompressible), pisoFoam (transient), interFoam (multiphase), etc.
2
Configure Numerics
Set discretization schemes (fvSchemes) and linear solver settings (fvSolution). Balance accuracy vs. stability.
3
Monitor Convergence
Track residuals — the measure of how well the equations are satisfied. Residuals should drop 3-4 orders of magnitude.
4
Parallel Execution
Decompose domain with decomposePar, run across multiple cores with mpirun, and reconstruct with reconstructPar.

## Slide 14
Introduction to OpenFOAM — Microcredential Module 1
14 / 28
Stage 3: Post-Processing
ParaView
Primary visualization tool. Create contour plots, streamlines, vector fields, iso-surfaces, and animations. Launched via paraFoam command.
Function Objects
Built-in runtime analysis: forces, pressure coefficients, field averages, probes, and sampling — all configured in controlDict.
Data Sampling
Extract data along lines, surfaces, or at probe points for quantitative comparison with experimental results.
Validation
Compare simulation results against analytical solutions, experimental data, or other CFD codes to verify accuracy.

## Slide 15
Introduction to OpenFOAM — Microcredential Module 1
15 / 28
OpenFOAM Case Structure

## Slide 16
Introduction to OpenFOAM — Microcredential Module 1
16 / 28
The 0/ Directory — Initial & Boundary Conditions
0/U (Velocity Field)
dimensions [0 1 -1 0 0 0 0];
internalField uniform (0 0 0);
boundaryField
{
inlet
{
type fixedValue;
value uniform (1 0 0);
}
outlet
{
type zeroGradient;
}
walls
{
type noSlip;
}
}
Key Elements
dimensions: SI unit dimensions of the field
internalField: Initial value throughout the domain
boundaryField: Conditions at each boundary patch
fixedValue: Dirichlet condition (set value)
zeroGradient: Neumann condition (zero derivative)
noSlip: Zero velocity at wall

## Slide 17
Introduction to OpenFOAM — Microcredential Module 1
17 / 28
The constant/ Directory
polyMesh/
points
List of all vertex coordinates
faces
Connectivity of vertices forming faces
owner
Cell owning each face
neighbour
Neighboring cell for internal faces
boundary
Boundary patch definitions
Physical Properties
transportProperties
Kinematic viscosity, density
turbulenceProperties
Turbulence model selection (laminar, RAS, LES)
thermophysicalProperties
Thermodynamic and transport models
g
Gravitational acceleration vector

## Slide 18
Introduction to OpenFOAM — Microcredential Module 1
18 / 28
The system/ Directory
controlDict
Master control file. Sets start/end time, time step (deltaT), write interval, solver application name, and runtime function objects.
fvSchemes
Discretization schemes for each term: time derivatives (ddtSchemes), gradients (gradSchemes), divergence (divSchemes), and Laplacian (laplacianSchemes).
fvSolution
Linear equation solver settings, tolerances, relaxation factors, and algorithm controls (SIMPLE, PISO, PIMPLE parameters).

## Slide 19
Introduction to OpenFOAM — Microcredential Module 1
19 / 28
OpenFOAM Solver Categories

## Slide 20
Introduction to OpenFOAM — Microcredential Module 1
20 / 28
Commonly Used Solvers
Solver | Type | Physics | Use Case
simpleFoam | Steady | Incompressible, turbulent | External aerodynamics
pisoFoam | Transient | Incompressible, turbulent | Vortex shedding
pimpleFoam | Transient | Incompressible, turbulent | General unsteady flows
icoFoam | Transient | Incompressible, laminar | Tutorial / simple cases
interFoam | Transient | Multiphase (VOF) | Free surface flows
rhoSimpleFoam | Steady | Compressible | High-speed flows
buoyantSimpleFoam | Steady | Heat transfer | Natural convection

## Slide 21
Introduction to OpenFOAM — Microcredential Module 1
21 / 28
Turbulence Modeling in OpenFOAM
RANS (Reynolds-Averaged)
Most Used
Time-averaged equations with turbulence models. Most common for engineering. Models: k-epsilon, k-omega SST, Spalart-Allmaras.
LES (Large Eddy Simulation)
High Fidelity
Resolves large eddies, models small ones. More accurate but computationally expensive. Models: Smagorinsky, WALE, dynamic.
DNS (Direct Numerical Simulation)
Research
Resolves all turbulent scales. Extremely expensive — only feasible for low Reynolds numbers and research.

## Slide 22
Introduction to OpenFOAM — Microcredential Module 1
22 / 28
Industry Applications

## Slide 23
Introduction to OpenFOAM — Microcredential Module 1
23 / 28
OpenFOAM vs. Commercial CFD
Feature | OpenFOAM | Commercial (e.g., ANSYS Fluent)
Cost | Free (GPL v3) | $20,000-$50,000+/year
Source Code | Fully accessible & modifiable | Closed / black box
GUI | Command-line (third-party GUIs) | Polished integrated GUI
Customization | Unlimited (C++ / Python) | Limited UDF/scripting
Scalability | No license limits on cores | License-limited parallelism
Support | Community + paid options | Vendor support included
Learning Curve | Steeper (Linux/CLI focused) | Gentler (GUI-guided)

## Slide 24
Introduction to OpenFOAM — Microcredential Module 1
24 / 28
Installation & Platforms
Native Linux
Best performance. Ubuntu is recommended. Install via package manager (apt) or compile from source.
Windows (WSL)
Run OpenFOAM through Windows Subsystem for Linux. Full functionality with native-like performance.
Docker Containers
Pre-configured containers for quick setup. Ideal for consistent environments across teams.
macOS
Compile from source or use Docker. Not officially supported but community solutions exist.

## Slide 25
Introduction to OpenFOAM — Microcredential Module 1
25 / 28
Running Your First Simulation
$ cd $FOAM_TUTORIALS
Navigate to tutorials directory
$ cp -r incompressible/simpleFoam/pitzDaily .
Copy the cavity tutorial case
$ cd pitzDaily
Enter the case directory
$ blockMesh
Generate the mesh
$ simpleFoam
Run the solver
$ paraFoam
Visualize results in ParaView

## Slide 26
Introduction to OpenFOAM — Microcredential Module 1
26 / 28
Community & Resources
Official Documentation
openfoam.com/documentation — comprehensive user guide, programmer guide, and tutorial guide.
CFD Direct Guide
doc.cfd.direct — extensive user guide for Foundation releases with practical examples.
OpenFOAM Wiki
Community-driven wiki with tips, tutorials, and troubleshooting guides.
Forum & Mailing Lists
cfd-online.com/Forums/openfoam — active community forum for Q&A and discussion.
YouTube Tutorials
Multiple channels offering step-by-step video tutorials for all skill levels.
Published Textbooks
Multiple textbooks available for structured learning, from beginner to advanced.

## Slide 27
Introduction to OpenFOAM — Microcredential Module 1
27 / 28
Key Takeaways
OpenFOAM is a powerful, free, open-source CFD toolbox used worldwide in industry and academia
It solves the Navier-Stokes equations using the Finite Volume Method (FVM)
Every simulation follows three stages: pre-processing, solving, post-processing
The case structure has three directories: 0/ (conditions), constant/ (properties), system/ (controls)
80+ built-in solvers cover incompressible, compressible, multiphase, heat transfer, and more
The open-source nature enables unlimited customization and zero-cost parallel scaling

## Slide 28
What's Next?
Complete the assessment activity to test your understanding
Take the Moodle Quiz to assess your understanding
Try the interactive H5P activities for hands-on learning
Set up OpenFOAM on your system
Run the lid-driven cavity tutorial case
Module 1 of OpenFOAM Microcredential